## Slide 1
P0
P1
P2
P3
P4
P5
P6
P7
P8
3.3V Rail (1A supply Max)
GND Rail
VIN (3.6V - 5V)
ADC
UART 3
TX
UART 3
RX
SPI 2
SCLK
SPI 2
MISO
SPI 2
MOSI
SPI 2
SS
I2C 2
SDA
I2C 2
SCL
OpenMV N6
Micro SD Slot
SD < 2GB Max
SDHC < 32GB Max
SDXC < 2TB Max
Pin
Name
Pin
Name
WKUP3
Reset (Connect to GND to reset)
Machine Module Peripherals / Timers
Machine Module Peripherals / Timers
All pins are 3.3V tolerant with a 3.3V output
All pins can sink or source up to 20 mA
By: Ibrahim Abdelkader & Kwabena W. Agyeman
https://openmv.io
CAN 1 RX
P9
TIM4 CH1
CAN 1 TX
P10
ETH LED
ETH RXN / DB N
ETH RXP / DB P
ETH TXN / DA N
ETH TXP / DA P
SW2 - WKUP2
RAW
GND Rail
TIM2 CH3
TIM2 CH4
UART4 TX
TIM4 CH2
TIM17 CH1
TIM15 CH2
3.3V Rail
BOOT 0
P13 – UART7 RX
P14 – UART7 TX
DD N
DD P
DC N
DC P
Frame Sync Input/Output
P11
RAW provides always-on unregulated (3.6V-5V) power in on/off or deepsleep modes.
Connect BOOT0 to 3.3V to put the board into recovery mode to reflash the bootloader.
SW
BOOT 1 SW
SW2
UART4 RX
I2S 2 SDO
I2S 2 SDI
I2S 2 CK
I2S 2 WS
I3C 2 SCL
I3C 2 SDA
TIM12 CH1